## Slide 1: MONITORING OF PULSED INTERMEDIATE-ENERGY NUCLEON BEEMS USING AIR ACTIVATION
V. M. Skorkin
INR RAS
LXXII International Conference "Nucleus-2022”, Moscow

## Slide 2: Use of pulsed beams of protons and neutrons
The intermediate-energy proton and neutron pulsed beams are used for radiation therapy at the proton accelerators and for science material studies at the neutron sources.
Secondary radiation from the interaction of the beam with biological targets, equipment and material is used to control the beam parameters and a absorbed dose.

## Slide 3: A neutron radiation from p beam losses in equipment
The evaporation neutron spectrum from p pulse losses.

## Slide 4: A monitoring system of a proton beam losses used neutron dose measured UDBN detector
The absorbed dose of the proton beam in cell cultures using Gafchromic film and the pulsed neutron flux using UDBN detector were measured.

## Slide 5: The 11C, 14N, 15O short life positron-emitter isotopes emittihg annihilation 511 keV photons
This gamma radiation from p pulse created in biological targets used to pulsed nucleon beam monitoring
γ , МeV | reaction
1.63 | 16O(p,xγ)14N
2.00 | 16O(p,xγ)11C
2.04 | 16O(p,xγ)15O
2.00 | 12C(p,xγ)11C

## Slide 6: A monitoring system of a proton beam losses used  - ray dose measured BDMG detector.

## Slide 7: The p pulse beam (1), local cell absorbed (2), neutron (3,4) and gamma (5) dose
1010 p pulse (30 μs) created 10 Gy cultures at the Bragg peak and the neutron dose is about 1 mSv (at 10 cm distance)

## Slide 8: Linear dependence of the absorbed dose of protons by cells (1) and the dose of neutrons (2,3) on the dose of gamma radiation

## Slide 9: The n spectrum from the cascade neutron pulsed source
The cascade neutrons have intermediate energy over 20 MeV.

## Slide 10: The scattered neutron spectrum on pulsed source
The neutron spectrum from cascade n scattering in pulsed source transporting channel.

## Slide 11: The - and - radiation from n and p irradiated material
A monitoring system of a proton beam losses used  - ray dose measured BDMG detector.

## Slide 12: The radiation dose from p pulse losses when interacting
The 1010 proton pulse create 1.6 mSv dose of the evaporation neutrons in channels for transporting a beam to targets.
The irradiation of the biological targets and materials with 1010 intermediate-energy proton and neutron pulse create 24 µSv dose of the gamma and beta radiation.

## Slide 13: MKS-01R radiometer for measurement of - and - radiation from n and p irradiated material and biological targets

## Slide 14: The - and - radiation from p pulse beam - and - radiation, measured MKS-01R radiometer on medical channel

## Slide 15: Time diagrams of the radiation, measured used MKS-01R radiometer on TOF neutron channel of pulsed source

## Slide 16: Air gaps in the proton and neutron channels
The channels for transporting p and n pulse beams have air gaps.

## Slide 17: The p and n pulsed beams interact with air atoms
It is in this gap that the irradiated samples with the elements under study and the detecting equipment are located. The air contains nuclei of nitrogen, oxygen, carbon and argon, in which medium-energy neutrons (20-200 MeV) create an intranuclear cascade with the emission of nucleons.
The residual nucleus is in a preequilibrium state in various partial-hole configurations at different excitation energies. Then the excited nucleus decays, including the evaporation of particles and the emission of gamma rays.

## Slide 18: Intermediate energy nucleons are non-elastically scattered by air atoms (nitrogen, oxygen, argon, etc.) and creates short-lived radionuclides (life tame from 20 ms to 100 s) in spallation process.
The residual nucleus is in a preequilibrium state in various partial-hole configurations at different excitation energies. Then the excited nucleus decays, including the evaporation of particles and the emission of gamma rays.

## Slide 19: Gamma and beta radiation from the decay of radionuclides can be used to pulsed nucleon beam monitoring
As a result of the activation of atoms 14N(99.6%), 15N(0.4%) in the reactions short-lived radionuclides are formed. As a result of reactions on carbon 12C(n, p)12B(20 ms) with a threshold of 14 MeV (0.2 mb) and 13C(n, p) 13B(19 ms) with a threshold of 13 MeV, isotopes with a lifetime of about 20 ms are formed.
In the reaction 16O(n, p)16N(7.1s) with a threshold of 3 MeV (41 mb) and 18O(n, p) 18N(0.6s), rapidly decaying radionuclides are formed.

## Slide 20: Thermal neutrons can activate air (14N, 80 mb) with the formation of capture gamma rays, which can also contribute to the background.
14N(99.6%)+n=3n +12N(11ms) +(16.4MeV)+ (511keV, 200% +4.43MeV, 2.4%)
3α(196 keV,3%)
15N(0.366%)+n= p +15C(2.45s,>80mb) +(16.4MeV)+ (511keV, 200% + 4.43 MeV, 2.4%)

## Slide 21: Activation monitor based on MKS-01R radiometer and а single-board microcomputer Raspberry Pi2 for on line pulsed n and p irradiation control
The sensitivity of the monitor to neutrons estimated from these data was about 0.02 - 0.1 pulses/(n/cm2).
The monitor allows to control pulsed beams of protons and neutrons with an energy of 20-200 MeV at a frequency of up to 50 Hz.

## Slide 22: The measurement of - and - radiation from p pulse beam on medical channel used MKS-01R radiometer

## Slide 23: Time diagrams of the radiation background, measured used MKS-01R radiometer on a medical channel

## Slide 24: The radiation measured used MKS-01R radiometer activated by p pulsed beam and on the medical channel

## Slide 25: Time diagrams of the radiation background on the pulsed neutron source

## Slide 26: Time diagrams of the gamma and beta radiation from an activated air on the pulsed neutron source

## Slide 27: Time diagrams of the neutron beam fluxes of the pulsed neutron source (a) and the gamma and beta radiation from activated air (b).

## Slide 28: On line monitoring pulsed neutron irradiation of composite protection material used MKS-01R radiometer RADEX

## Slide 29: The scattering proton dose control used scintillation detector
System for measuring intensity of scattering protons from p pulse with accuracies of 1%
The dose irradiated personal from 1010 p pulse scattered by the CH2 target (1 сm) was 1 mGy.